## Slide 1: Balsa Glider Construction

## Slide 2: Balsa Glider Construction

## Slide 3: Balsa Wood
Very high strength-to-weight ratio
Easy to cut and sand
Grainy
Available in strips, sheets, or blocks
Not very durable for a fuselage . . . spruce is better

## Slide 4: Glider Components
Fuselage
Wings
Horizontal stabilizer
Vertical tail (or stabilizer)
Nose weight

## Slide 5: Familiarize Yourself with the Plan
Components
Dimensions
Materials
Outlines vs. cuts

## Slide 6: Building on a Single Sheet
Wing
Horizontal
Stabilizer
Vertical
Tail
Notice the grain direction: Always spanwise!
Leave extra space at these locations if material allows

## Slide 7: Marking the Fuselage
Wing
Location
Center
of
Gravity
Neutral
Point
Horizontal
Stabilizer
Vertical
Tail
Cut for Length

## Slide 8: Choosing a Wing Planform
Elliptical wings might be great for full size aircraft, but they are challenging for small gliders
Straight leading edges tend to work well for small gliders

## Slide 9: Cut Out Pieces
Cut the wing with extra span if material allows (see later note for reason)
Cut out stabilizers
Sand leading and trailing edges with minimal rounding

## Slide 10: Finish Trailing Edge
Trailing edge imperfections most often occur at wingtips
If material allows, finish trailing edge then make final cuts for span and/or leading edge curvature

## Slide 11: Shaping the Wing Profile
Leading edge should have minimal rounding
Trailing edge needs taper on top only
Use sanding block and edge of a solid surface for uniform sanding

## Slide 12: Adding the Wing
Center the wing on the fuselage
Glue it on straight and square to the fuselage . . . this is critical

## Slide 13: Making a Strong Bond
Avoid typical novice method of applying excessive glue on an edge and sticking material together
Light bond with reinforcing fillets increases the glue surface area and bond strength

## Slide 14: Add Horizontal Stabilizer
One piece stabilizer
  Stronger
  Only possible if mounted somewhere away from vertical stabilizer
Two piece stabilizer
  Weaker
  Mount anywhere else

## Slide 15: One Piece Stabilizer
Cut out wedge from glider plan
Trace on to fuselage wood scrap, then cut out wedge
Glue wedge (not stabilizer) to top of fuselage (direction dependent upon tail or canard mount)
Front
Back
Side of Fuselage
HS
Wedge
Stabilizer
Canard Position
HS
Front
Back
Tail Position
HS

## Slide 16: Check Alignment
Hold stabilizer on wedge
Ensure from front or back that stabilizer is parallel to wing
If not, sand wedge slightly and recheck

## Slide 17: Glue Stabilizer
Cut out wedge from the glider plan
Trace angled line onto side of fuselage
Direction dependent on tail or canard mount

## Slide 18: Two Piece Stabilizer
Cut out wedge from glider plan
Trace angled line onto side of fuselage
Direction dependent on tail or canard mount
Canard Position
HS
Wedge
Front
Back
Side of Fuselage
HS
Tail Position
HS

## Slide 19: Check Alignment
Cut stabilizer in two
Glue one side at a time to each side of fuselage
Canard Position
HS
Tail Position
HS

## Slide 20: Glue Stabilizer
Glue to SIDE of fuselage
Make certain that each half is straight and square to fuselage

## Slide 21: Vertical Stabilizer Side Mount
Requires tail at a completely different location on fuselage from horizontal stabilizer
Glue onto side of fuselage flush with bottom edge and front edge even with vertical tail mark
VT
Front
Back
Side of Fuselage
VT
Top View
VT

## Slide 22: Vertical Stabilizer Top Mount
Can be used no matter where tail is located
Draw line down center of fuselage top starting at vertical tail mark
Glue on vertical tail straight and square
VT
Front
Back
Side of Fuselage
VT
Top View
VT
VT

## Slide 23: Balance the Glider
Place pencil on table top and put glider on top of it with center of gravity directly over pencil
Add clay to nose until glider balances at the center of gravity

## Slide 24: Balance the Glider
Hold glider on fingertips placed at nose and tail
Add clay to wingtips until glider balances at fuselage

## Slide 25: Wings with Dihedral?
Prior to gluing to fuselage:
  Completely finish and sand wing
  Put wing vertical with its trailing edge flat on a smooth, level surface such as glass

## Slide 26: Making Cuts
Put triangle at dihedral cut locations
Use sharp blade
Hold triangle firmly to the wing and cut partially through wing
Do this at each location (must be parallel cuts)

## Slide 27: Assemble Wing
Put wax paper on glass surface
Hold wing panels together
Wick glue into wing joint (e.g., CA adhesive)
Complete polyhedral then central joint

## Slide 28: Final Assembly
Dihedral may require cutting a shallow v-shaped trough into top of fuselage to maintain dihedral angle