## Slide 1: Multi-View Sketching

## Slide 2: Multi-View Drawing
Shows two or more two-dimensional views of a three-dimensional object.
Provides the shape description of an object.
When combined with dimensions, serves as the main form of communication between designers and manufacturers.

## Slide 3: Multi-View Drawing

## Slide 4: Multi-View Drawing
All three-dimensional objects have width, height, and depth.
  Width is associated with an object’s side-to-side dimension.
  Height is associated with an object’s top-to-bottom dimension.
  Depth is associated with front-to-back distance.

## Slide 5
Multi-View Drawing
TOP VIEW
FRONT VIEW
RIGHT SIDE VIEW
Notes: A typical multi-view drawing includes a top view, a front view and a right side view.

## Slide 6
45°
Multi-View Drawing
Notes: The isometric view shows the width, height and depth of the object. The height of the object is obvious in the front view and the right side view. The width is displayed in the front view and the top view. And the depth is shown in the top and right side. Notice how all views are aligned such that line up and construction lines can be used to help project the views from the first view drawn.

## Slide 7
Orthographic Projection
A technique used to create Multi-View drawings.
Any projection of the features of an object onto an imaginary plane of projection.
  The projection of the features of the object is made by lines of sight that are perpendicular to the plane of the feature

## Slide 8
The best way to understand orthographic projection is to imagine an object contained inside a glass box.
Orthographic Projection

## Slide 9
There is a total of six glass walls surrounding the object. Each wall represents a projection plane onto which a two- dimensional object view will be created.
Orthographic Projection
Notes: Tell Students: Notice the six glass walls that represent planes and six views can be projected from this view. Three views are typically used and they are top, front, and right side. The opposite of each view being bottom, back, and left side also exist.

## Slide 10
Also referred to as a plane of projection or picture plane, is an imaginary surface that exists between the viewer and the object.
The surface onto which a two-dimensional view of a three-dimensional object is projected and created.
Projection Plane

## Slide 11
Start by focusing only on the front projection plane.
A person standing in front of the object would see only the five corners identified in black.
1
2
3
4
5
line of sight
at 90° angle to projection plane
Orthographic Projection

## Slide 12
Projection lines are used to project each corner outward until they reach the projection plane.
Orthographic Projection

## Slide 13
An imaginary line that is used to locate or project the corners, edges, and features of a three-dimensional object onto an imaginary two-dimensional surface.
Projection Line

## Slide 14
The visible edges of the object are then identified on the projection plane by connecting the projected corners with object lines.
Orthographic Projection

## Slide 15
The orthographic projection process is then repeated on the other projection planes.
Orthographic Projection
Notes: There are six principle planes as indicated here. In most cases, three or fewer orthographic projections are needed in a multi-view in order to fully describe and object.

## Slide 16: View Selection
Recommendations for how to select the front view
  Most natural position or use
  Shows best shape and characteristic contours
  Longest dimensions
  Fewest hidden lines
  Most stable and natural position
Notes: The view of the side that provides the most information about the object is generally chosen as the FRONT view. Finding the best front view of a part can be difficult. Two or more sides may look like the best solution for a front view.
These are the same recommendations given in the Oblique and Isometric Pictorial presentation.
When selecting a front view, compare all side views and choose a front view based on the list of criteria in this list.

## Slide 17: Orthographic View Selection
BEST FRONT VIEW
Best shape
Description
Longest Dimension
Most natural position
No hidden edges
Notes: The front view choice dictates the pictorial orientation as well as the orthographic projection labels.

## Slide 18: Number of Orthographic Projections
Recommendations for how to select the front view
  Most natural position or use
  Shows best shape and characteristic contours
  Longest dimensions
  Fewest hidden lines
  Most stable and natural position
Notes: In addition to selecting the best front view, you must decide how many views are required to fully describe an object. In many cases, three views (Top, Front and Right Side). But sometimes less views are required in order for the part geometry to be correctly interpreted.

## Slide 19: Number of Orthographic Projections
One View
Uniform thickness or shape
Two views would be identical
All dimensions properly and easily shown on one view
Notes: Only one view may be required if the part has a uniform thickness (such as a flat plate) or a uniform shape (such as a cylindrical shape).
If two views would be identical and all dimensions are easily shown on one view, additional views may not be necessary.

## Slide 20: Number of Orthographic Projections
Two Views
Symmetrical part
A third view would be identical to one other
Second view is necessary for depth
Notes: Only two views may be required if the part is symmetrical such that a third view would be identical to another. However a second view is necessary to show a depth that is not constant.

## Slide 21
Given the overall dimensions of the object, a pencil, and a sheet of graph paper, a sketching multi-view drawing can be easily done using points, construction lines, and object lines.
Sketching a Multi-View Drawing
Notes: There are several ways to sketch a multi-view drawing. Feel free to use the best way that make since to you. Teachers may choose to explain from the board or overhead using an example and have students follow along.

## Slide 22
Sketching a Multi-View Drawing
Step 1 - Layout the boxes within which the individual views will occur using points and construction lines.
FRONT
TOP
RIGHT SIDE

## Slide 23
Sketching a Multi-View Drawing
Step 2 - Use construction lines between the views to indicate the geometry of the views.
Notes: Three examples of edges that are translated to construction lines are shown here.

## Slide 24
Sketching a Multi-View Drawing
Step 3 - Identify the visible edges with Object lines.

## Slide 25
Sketching a Multi-View Drawing
Step 4 - Locate hidden lines.

## Slide 26
Leonard P. Karr (1913-1995) designed a man-sized hunting blind shaped like a goose called Super Goose, 1991.
Historical Example
How would you label the views presented in the drawing?
Are Mr. Karr’s views properly aligned based on the orientation presented here?
How would you rearrange the views to orient

## Slide 27
A Question…
Each of the blocks at right has the same overall dimensions and color. What else do they have in common?
Notes: You could have students practice sketching the multi-view drawings of these objects individually or in groups to help determine the answer before revealing it.

## Slide 28
A Question…
Each of the blocks at right has the same overall dimensions and color. What else do they have in common?
They all have identical top views!